I am measuring motor temperature. An RTD is connected to the motor and I like to transmit the data to a PLC located off site over the Modbus communication. A PLC may be used to control the load to the motor or to shut down the motor as needed to prevent burnout.

M-System’s Mini-M model M2XUM is a universal input signal conditioner with Modbus RTU communication output.

M2XUM is also incorporated with analog output. The load resistance is available max. 750Ω with the 4-20mA output which can drive a local indicator.

.

| Standard | Conforms to RS-485, EIA |
| --- | --- |
| Transmission distance | 500 meters max. |
| Baud rate | 38.4 kbps max. |
| Communication | Half-duplex, asynchoronous, no procedure |
| Protocol | Modbus RTU |
| Transmission media | Shielded twisted-pair cable (CPEV-S 0.9 dia.) |

### Circuit Diagram of model M2XUM

M-System has flexible solutions to meet your specific application and requirements. Consult our Signal Conditioners Data Library. 