One of the model AYDV’s input signals is limited to 1-5 Vdc. When a customer needs to have both inputs 4-20 mAdc can we use the Resistor Module (model REM)?

As shown in the figures, the REM cannot be mounted between the terminals 4 and 6. In order to solve this problem, you can use another kind of resistor module model MU2. When you order, specify the AYDV-6A_ _-_ for the 1-5 Vdc, and the MU2 separately from the unit.

Connection diagram

M-System has flexible solutions to meet your specific application and requirements. Consult our Signal Conditioners Data Library. 